## Slide 1: Architecture: Building Blocks, Real-Time Issues, and Schedulability
Mike Whalen
University of Minnesota Software Engineering Center
Andrew Gacek, John Backes, Darren Cofer
Rockwell Collins Advanced Technology Center

## Slide 2: Overview of Topics
Building from AADL
  Active and Passive Tasking Model
  Minor Interface Changes
Schedulability Analysis
“Headless” OSATE build
Testing and Integration

## Slide 3
Datalink
Radio UART
Decrypt
GCS Receive

## Slide 4: Phase I Architecture
Pros: Good Functional Design Principles
  Small, cohesive tasks
  Low coupling via message passing
Cons: Analysis
  Schedulability
    Internal-event scheduled processes do not have bounded min-dispatch times
    Large numbers of OS-scheduled processes make RTOS context switch slow
  Latency
    Bounding end-to-end time for information to flow through the system?
    Significant possible jitter if priorities are mis-aligned
  Behavioral Analysis:
    Interleavings and queueing behavior causes state explosion for automated analysis tools

## Slide 5: An Example
Six tasks: {A, B, C, D, E, F}
Tasks communicate using event ports that send messages
  Also communicate using shared variables, but these do not cause dispatch
A
C
E
B
D
A
F
Periodic: 100ms
Sporadic: IRQ with min dispatch interval: 1ms

## Slide 6: Phase 1 Approach
Lots of queueing
Lots of asynchrony
No deadlock though livelock is possible
Assigning priorities is tricky and can lead to jitter
Aperiodic threads are difficult to schedule
A
C
E
B
D
A
F
Thread 1
Periodic: 100ms
Aperiodic
Aperiodic
Aperiodic
Aperiodic
Sporadic: IRQ with min dispatch interval: 10 ms
Thread 2
Thread 3
Thread 4
Thread 5
Thread 6

## Slide 7: Phase II Architectural Principles
Preserve “good” cohesion and coupling
  This is really nice in Phase I!
Provide better analysis support
  Schedulability analysis using std. approaches
    RMA or EDF
  Mechanisms for measuring flow latency / jitter
  Reduce asynchrony for scalable behavioral analysis

## Slide 8: Phase 2 Approach
A
C
E
B
D
A
F
Periodic: 100ms
Passive
Passive
Passive
Passive
Sporadic: IRQ with min dispatch interval: 1 ms
T2
T1
Passive tasks are Hoare-style monitors
Communication to passive tasks: synchronous calls
Fewer OS-scheduled threads / less asynchrony

## Slide 9: Phase 2 Approach
A
C
E
B
D
A
F
Periodic: 100ms
Passive
Passive
Passive
Passive
Sporadic: IRQ with min dispatch interval: 1 ms
T2
T1
Communication to active tasks: queued as in Phase I
Possibility of Deadlock!

## Slide 10: Phase 2 with RPCs
A
C
E
B
D
A
F
Periodic: 100ms
Passive
Passive
Passive
Passive
Sporadic: IRQ with min dispatch interval: 1 ms
T2
T1
Want to avoid deadlock and minimize resource contention
Naïve approach: Standard RPCs
  Resource contention length is sum of WCETs of longest contention chain
  Deadlock possible if circular communications between threads

## Slide 11: Phase 2 with Queued RPCs
A
C
E
B
D
A
F
Periodic: 100ms
Passive
Passive
Passive
Passive
Sporadic: IRQ with min dispatch interval: 1 ms
T2
T1
Want to avoid deadlock and minimize resource contention
Queued RPCs: Queue events until monitor complete and semaphore released
Resource contention is then WCET of single monitor

## Slide 12: Queued RPCs

## Slide 13: Visualizing an Execution Sequence
A
C
E
B
D
A
F
Periodic: 100ms
Passive
Passive
Passive
Passive
Sporadic: IRQ with min dispatch interval: 1 ms
T2
T1
Want to avoid deadlock and minimize resource contention
Queue events until monitor complete
Resource contention is then WCET of single monitor

## Slide 14: Schedulability Analysis with RMS
A
C
E
B
D
A
F
Periodic: 100ms
WCET: 50us
Passive
WCET: 1ms
Passive
WCET: 1 ms
Passive
WCET: 20us
Passive
WCET: 200us
Sporadic: IRQ with min dispatch interval: 1 ms
WCET: 50us
T2
T1
OS Task Switch:
10us
From component writers, we need:
maximum number of outgoing events per port per task dispatch
WCET for each task
Dispatch type and min-interval for active threads
Maximum time / dispatch rate for First Level Interrupt Handlers
1
1
2
1
1
1
From OS, we need:
Task switch time (preemption overhead)
Mutex lock time

## Slide 15: Schedulability Analysis with RMS
A
C
E
B
D
A
F
Periodic: 100ms
WCET: 50us
Passive
WCET: 1ms
Passive
WCET: 1 ms
Passive
WCET: 20us
Passive
WCET: 200us
Sporadic: IRQ with min dispatch interval: 1 ms
WCET: 50us
T2
T1
OS Task Switch:
10us
Thread 1 has low priority. T1 WCET: 100us + 1ms + 2*(1 ms + 20us + 200us) + 20us + 200us = 3760us
Thread 2 has high priority. T2 WCET: 50us + 20us + 200us = 270us
Maximum blocking time for thread 1: execution of Task F (200us)
+ time for context switches + mutex lock/unlock
1
1
2
1
1
1

## Slide 16: Latency Analysis
A
C
E
B
D
A
F
Periodic: 100ms
WCET: 50us
Passive
WCET: 1ms
Passive
WCET: 1 ms
Passive
WCET: 20us
Passive
WCET: 200us
Sporadic: IRQ with min dispatch interval: 1 ms
WCET: 50us
T2
T1
OS Task Switch:
10us
If on one thread (active task), can be computed from WCET
If crossing multiple threads, can be bounded (future work)
1
1
2
1
1
1

## Slide 17: AADL Properties for Build
thread E
features
Input1: in event data port Base_Types::Unsigned_32 {
SMACCM_SYS::CommPrim_Source_Header => "E_Handlers.h";
SMACCM_SYS::CommPrim_Source_Text => "E_Handlers.c";
SMACCM_SYS::Compute_Entrypoint_Source_Text =>
("eventhandler_E_Input1");
};
Output1: out event data port Base_Types:: Unsigned_32 {
SMACCM_SYS::CommPrim_Source_Header => "E_Output.h";
SMACCM_SYS::CommPrim_Source_Text => "E_Output";
};
Output2: out data port Base_Types:: Unsigned_32 {
SMACCM_SYS::CommPrim_Source_Header => "E_Output.h";
SMACCM_SYS::CommPrim_Source_Text => "E_Output";
};
properties
SMACCM_SYS::Language => "Ivory";
SMACCM_SYS::Thread_Type => Passive ;
Compute_Execution_Time => 5 us .. 30 us;
SMACCM_SYS::Sends_Events_To => "{{1 Output1, 1 Output2}, {2 Output 2}}";
end E ;
Thread Type: Active or Passive
Compute_Execution_Time: BCET .. WCET
Sends_Events_To:
List of sets of comma separated {<number> <port>} pairs
In this case, the thread can send one message to each of Output1 and Output2, or two messages to Output2

## Slide 18: AADL Properties for Build
thread A
features
Output1: out event data port Base_Types:: Unsigned_32 {
SMACCM_SYS::CommPrim_Source_Header => "A_Output1.h";
SMACCM_SYS::CommPrim_Source_Text => "A_Output1";
};
Output2: out event data port Base_Types:: Unsigned_32 {
SMACCM_SYS::CommPrim_Source_Header => "A_Output2.h";
SMACCM_SYS::CommPrim_Source_Text => "A_Output2";
};
properties
Dispatch_Protocol => Periodic;
Period => 100 ms;
Source_Text => ("eventhandler_periodic_A.c");
Priority => 45;
Stack_Size => 2048 bytes;
SMACCM_SYS::Language => "Ivory";
SMACCM_SYS::Thread_Type => Active ;
Compute_Execution_Time => 10 us .. 50 us;
SMACCM_SYS::Sends_Events_To => "{{1 Output1, 1 Output2}}";
end A ;
Active threads have a dispatch protocol: Periodic or Sporadic (for event-based threads). If periodic, then a period must be specified
Active threads must have a specified stack size. This is currently the aggregate required stack for all passive object invocations; we could modify this so that it is computed from stack sizes of each passive object.

## Slide 19: Implementations
eChronos:
  All tasks in one memory space
  Implementation: procedure calls with mutex for mutual exclusion
  Sends_Events_To property used to determine maximum queue depth for each outgoing interface.
  Queued communications same as Phase I
CAmkES
  Tasks in separate memory spaces
  Active/passive tasks correspond closely to CAmkES active/passive components
  However, to support queued synchronous calls, scheduler component is constructed for each thread to actually perform dispatching to tasks

## Slide 20: AADL  CAmkES Overview
All threads (active or passive) become components
data ports in AADL become dataports of the same type.
  Need mutual exclusion for complex types.
Event/event data ports become:
  If destination is active thread: dataport containing queue for destination (matching Phase I eChronos)
  If destination is passive thread: RPC interface with message as argument.
AADL RPC ports are translated into CAmkES procedures (for interface) and uses/consumes.
Priorities are described in the configuration

## Slide 21: CAmkES Implementation
thread A
features
Output1: out event data port Base_Types:: Unsigned_32 {
SMACCM_SYS::CommPrim_Source_Header => "A_Output1.h";
SMACCM_SYS::CommPrim_Source_Text => "A_Output1";
};
Output2: out event data port Base_Types:: Unsigned_32 {
SMACCM_SYS::CommPrim_Source_Header => "A_Output2.h";
SMACCM_SYS::CommPrim_Source_Text => "A_Output2";
};
properties
Dispatch_Protocol => Periodic;
Period => 100 ms;
SMACCM_SYS::Compute_Entrypoint_Source_Text =>
("eventhandler_periodic_A1”, "eventhandler_periodic_A2”,);
… more stuff here
end A ;
AADL Model:
CAmkES component:
component A {
control;
uses Unsigned_32_Receiver A_Output1;
uses Unsigned_32_Receiver A_Output2;
consumes sig sig_period;
dataport buffer b2;
}
Generated C code
void main() {
uint32 time = get_system_time();
eventhandler_periodic_A1(time);
eventhandler_periodic_A2(time);
}
CAmkES config:
I don’t know how to do this yet!!
- Priority
- Stack Size
- Setting up interaction with system resources (timer interrupt)
- Binding C code into make
CAmkES interface:
procedure Unsigned_32_Receiver {
void the_proc(in int arg);
}

## Slide 22: CAmkES Implementation Qs
Tower parameter passing conventions vs. CAmkES parameter passing conventions
  AADL generation matches Tower
How should we set up periodic task dispatch?
  Dispatcher as signaler:
    All periodic tasks are control components
    Dispatcher signals each periodic task at appropriate time
    Matches eChronos model
  Dispatcher as executor:
    All periodic tasks are passive components
    Dispatcher executes tasks sequentially based on periodic argument
Send/Receive primitives between threads in CAmkES
  Can we send complex types?
  Can we specify queues with certain depth?

## Slide 23: Build Mechanics
Headless version of aadl2rtos for Eclipse using RAMSES
  “Standard” headless build tool for OSATE
  Supports command line build
  Like to integrate into Phase I build
For eChronos: added support for two-level interrupt handlers and multiple ISRs per thread:
Input1: in event data port Base_Types::Integer {
SMACCM_SYS::CommPrim_Source_Header => "Signal1_Handlers.h";
SMACCM_SYS::CommPrim_Source_Text => "Signal1_Handlers.c";
SMACCM_SYS::Is_ISR => true;
SMACCM_SYS::Signal_Name => "signal1";
SMACCM_SYS::First_Level_Interrupt_Handler => "flih_signal1";
SMACCM_SYS::Compute_Entrypoint_Source_Text => ("eventhandler_signal1_1, eventhandler_signal1_2");
};

## Slide 24: Issues
Stack usage: deep passive task chains lead to large stack requirements for active threads
  On the other hand, we get rid of most input queues
  Similar “global” memory requirements
  Migration of use from static segment to stack
Response time vs. # of active processes
  May want periodic processes immediately following “fast”
Direct support for RPCs
  Easy on CAmkES. Necessary for eChronos?
Getting to system services in CAmkES
  Mutexes for active thread communications
  Drivers or direct access to ISRs
CAN bus(!)
Critical and non-critical tasks and priorities

## Slide 25: Questions?